## Slide 1: Group 5 amo-cobbia kofi ntiamoah maxwell agyemang duah francis quansah paul

## Slide 2: Content
Components
Schematics
Mode of operation

## Slide 3: Smart Water leakage Detection

## Slide 4: Components
Piezo
Ultrasonic distance sensor
Resistors
LED
Pushbutton
Breadboard
Arduino Uno R3

## Slide 5: schematics
The Arduino Uno R3 is a microcontroller that reads data from the ultrasonic sensor and buttons, controls the LED and buzzer accordingly.
The ultrasonic distance sensor(4 pin)
VCC serves as the power(5V)
GND:Ground
TRIG : It triggers pin to send ultrasonic pulses
ECHO: It receives reflected pulses
LED: Visual indicator for leakage

## Slide 6
Piezo buzzer: Sounds an alarm to detect water leakage
220 ohms resistor: protects the LED from execessive current
Push button: Manual reset or activation

## Slide 7: Mode of operation

## Slide 8
We decided to use an ultrasonic distance sensor to diagnose water leakages.
Firstly we initialize all of the necessary components .
Next an instruction of a loop is used whereby short pulses from the ultrasonic sensor are sent out from the trigger pin. Then the duration for how long the echo pin stays high is measured. A formula is inserted which helps us determine the distance and is displayed.
The leak detection logic is such that when the distance is less than 40 cm, it assumes that the water is too close ie. There is a leakage. Also if the distance is greater than 250,it assumes that the tank is empty and that there is a leak. In either case the buzzer goes off and the LED turns on. Otherwise the system is normal and both the LED and buzzer stay off.